These equations let you size a single stage craft and find the payload (if any) for a given mission profile (ΔV, TMR)
T = {F cdot ( 1-e^{-%DELTA V/V_e} )} over { TMR cdot (R-1) } newline P = { F } over { TMR } - E - R cdot T
And these equations determine the optimum (maximum ΔV) fuel split between two stages with fixed maximum mass. Note that TMR requirements are not considered. The optimal split cannot be followed for most launch vehicles because upper stages will tend to have insufficient TMR.
a = -V_el T^2 R (R-1) newline b = T(E_u+P)(V_eu(R-1)^2-V_el(R+1)(R-1)) newline c = V_eu(R-1)(E_u+P)(E_u+E_l+T+P+S)-V_el(R-1)(E_u+P)^2 newline newline x = {-b+sqrt{b^2 - 4ac}} over {2a}
In practice, one can find maximum practical lower stage tankage of a launcher by
RT(1-x) = {TMR_l} over {F_l} - { TMR_u } over { F_u } - S - E_l
At which point, the upper stage options simplify to the single stage case (albeit with some of the ΔV already taken care of).
Variable(s)	Meaning
ΔV	Change in velocity (“delta-vee”)
E	Engine mass (single stage)
Eu	Engine mass (upper stage)
El	Engine mass (lower stage)
F	Maximum thrust (“force”)
P	Payload mass
R	Mass ratio of tankage. 9 for most stock rocket tanks, 8 for Mk2/3 fuselages.
S	Extra stage mass (the penalty from having a stage, typically a decoupler).
T	Tankage mass (dry)
TMR	Thrust to Mass Ratio (N/kg or m/s2)
Ve	Effective exhaust velocity (9.80665 m/s2 * Isp in s),
Vel	Effective exhaust velocity of the lower stage
Veu	Effective exhaust velocity of the upper
x	Fraction of tankage mass in the upper stage
1-x	Fraction of tankage mass in lower stage
RT	Fully fueled tankage mass.
Tx	Upper stage empty tankage mass
RTx	Upper stage fully fueled tankage mass
T(1-x)	Lower stage empty tankage mass
RT(1-x)	Lower stage fully fueled tankage mass